## Slide 1: Internet of Things
Module 6, Lesson 1:
What is IoT

## Slide 2
What is IoT?
Basic concepts of IoT
Infrastructure of IoT
Topics

## Slide 3
Objectives
By the end of this lesson you should be able to:
    Understand Internet of Thing
    Understand IoT concept and Infrastructure

## Slide 4: What is IoT?
Intelligent interactivity between human and things to exchange information & knowledge
A global infrastructure for the information society, enabling advanced services by interconnecting (physical and virtual) things1.
1. http://www.itu.int/en/ITU-T/gsi/iot/Pages/default.aspx
Notes: Notes:
A key concept of Internet of Things (IoT) is a Thing that does something useful to make Internet of Things happen.
References:
http://www.itu.int/en/ITU-T/gsi/iot/Pages/default.aspx
image source: http://iotinnovator.com/liebherr-domestic-appliances-collaborates-microsoft-build-new-smart-fridge-medicine/

## Slide 5: What is IoT? (Cont.)
Sensor
Thing
Gateway
Cloud computing
Event
Feedback
Notes: Notes:
Establish bi-directional communication with millions of IoT devices.
  A thing – does something useful.
  A sensor – computes and communicates attached to the thing.
  A gateway – collects data from the thing.
  Cloud computing – analyzes data from sensor and providing feedback to the thing.
References:
Image source: https://1.bp.blogspot.com/-OpDDrfKKBV4/VrK5cPNS0RI/AAAAAAAALBk/1nEQTIRThY4/s1600/AzureIoTOnGA.PNG

## Slide 6: What is IoT? (Cont.)
Key Words and Concept of Internet of Things
Concept | Description
Things | Sense, Compute, Communicate and Act
Network (Infrastructure) | Web of things, Internet of Everything, Cloud Networks
Data | Collect, analyze and act upon
Notes: Things have to be useful and secure, authenticated and authorized.
They also have to be very low power.

## Slide 7
Storage / Management
Applications
Raw data retrieval
Preprocessing / Reasoning
Sensors
Acting Subsystem
Thinking Subsystem
Sensing Subsystem
Abstract Layer of IoT
Notes:   Notes:
  There are 3 subsystems in the Abstract layer of IoT. The 3 subsystems need to be connected to each other.
  The distribution of each of these components depend on the application.
  An application might have its own thinking & sensing subsystems.
Each subsystem:
  must be complex and decoupled from each other, or tightly integrated into 1 service.
  itself be a collection of distributed components
  can interact with another subsystems without knowing the underlying details.

## Slide 8
3 different approaches to acquire contextual information
    Direct sensor access
    Middleware infrastructure
    Context server
Sensor layer
Notes: Notes:
Direct sensor access
  Used in devices with sensors locally built in.
  The client software gathers the desired information directly from these Sensors.
  It is not suited for distributed systems.
Middleware infrastructure
  Introduces a layered architecture with the intention of hiding low-level sensing details.
Context server
  Distributed approach extends the middleware based architecture by introducing an access managing remote component.
  Gathering sensor data is moved to the context server to facilitate concurrent multiple access.

## Slide 9
Responsible for the retrieval of raw context data
    Makes use of appropriate drivers for physical sensor and APIs for virtual and logical sensors.
    The query functionality is often implemented in reusable software components.
Raw Data Retrieval

## Slide 10
Responsible for reasoning and interpreting contextual information
  The sensors queried in the underlying layer most often return technical data that are not appropriate to use by application.
  This layer raises the results of layer two to a higher abstraction level. The transformations include extraction and quantization operations
Preprocessing & Reasoning
Notes:   Notes:
  The single information can be combined to high-level information, for more precious and accurate.
The problem of sensing conflicts might occur when using several data sources has to be solved in this layer.

## Slide 11
            Clients may gain access in two ways:
                Synchronous mode
                Asynchronous mode
Storage and Management
Organizes the gathered data and offers them to the client via a public interface
Notes: Notes:
Synchronous mode : A Client sends a requesting message and pauses until it receives the server’s answer. (polling method)
Asynchronous mode : Each client subscribes to specific events it is interested in. (subscriptions method)

## Slide 12
The client is realized in this layer.
    The actual reaction on different events and context-instances is implemented in this layer
    Sometimes information retrieval and application specific context management and reasoning is encapsulated in form of agents
Application Layer
Notes: Notes:
The agents communicate with the context server and act as an additional layer between the preprocessing and the application layer.

## Slide 13: Sensor
A Large variety of sensors :
  Light, acceleration, location, temperature, biological signals, infrared, so on
Combination of multiple sensors
Sensors come in all kinds of flavors and can be combined
Notes: Notes:
Sensors :
  Provide a means to acquire data or information about the physical world
  Used to determine actions
  Combination of multiple sensors – more information to reason with and provide a more comprehensive view
  Providing a bridge between the physical world and the virtual world of a computer system.

## Slide 14: Sensor Types
                Physical Sensors
                Virtual Sensors
                Logical Sensors
                Sensor fusion
Notes: Notes:
Physical sensors : only hardware sensor, capturing any physical data.
Virtual sensor : context data from software application or services. Ex) users activity by checking for mouse movement.
Logical sensor : understand the context using two or more in combination of the DB. Ex) Login information – check the user authorization.
Sensor fusion : combine data from multiple sensors, and related information from associated databases, to achieve improved accuracies and more specific inferences.

## Slide 15: Sensor fusion
Techniques – detection, classification, identification of objects
    Taking observation from a number of sensors
    Solving equations to find values for variable
    Mathematical equations relate sensor observations with known quantities and variables to be discovered

## Slide 16: Classification of Sensors
Type of context | Use Sensors
Light | Photodiodes, color sensors, IR and UV-sensors etc.
Audio | Microphones
Motion, Acceleration | Mercury switches, angular sensor, accelerometers, motion detectors, magnetic fields
Location | GPS, Global system for mobile communications, Active badge system, etc
Physical attributes | Biosensors to measure skin resistance, blood pressure

## Slide 17: Sensing (Context Acquisition)
Context Attributes
Attribute | Description
Location | an entity’s position
Identify | unique identifier
Activity | status
Time | timestamp

## Slide 18: Sensing (RFID)
RFID (Radio Frequency Identification) tags or smart labels
    Can be read from or written to, using RFID reader with energy from a radio frequency field.
        RFID Tag
        RFID Reader

## Slide 19: Sensing (Location)
Location is widely used type of context in application.
Location Sensing | Description
GPS (global positioning system) | Use satellites, several meters accuracy
Mobile Phone Network | Suburb or town, 150~300 meter accuracy
WLAN | Triangulation with multiple access points, 1~2 meter accuracy
Bluetooth | short-range networking
Ubisense Sensor | for a tagged person, 15 cm accuracy

## Slide 20: Sensor usage
Where to put sensor
    Depends on the application and the type of sensor
    Embedded in the environment as part of the room, car, or worn on people
    Used to detect activities within an environment
Notes: Notes:
For example, Smart Car
  Wiper
  Headlight switch
  Cruise control
  Drowsy driver warning
  Car telematics
  Parking & Driving aids

## Slide 21: Infrastructure for IoT
Infrastructure
  A well established, pervasive, reliable, and publicly accessible set of technologies that acts as a foundation for other systems.
A Middleware layer
  Between sensors on one side and devices and applications on the other
Notes: Notes:
The layered architecture subsystems can be abstracted into an infrastructure.
The middleware presents a uniform layer of abstraction, making it easier to update individual pieces independently of each other.

## Slide 22: Infrastructure for IoT (Cont.)
Context
Service
Sensor
Sensor
Sensor
Sensor
Sensor
Sensor
Device
Apps
Device
Apps
Device
Apps

## Slide 23: What makes IoT possible
Integrated circuits technologies
  Miniature
  High computing power
  Low power
Wireless Technologies
  Reaching everywhere
  Low power
Networks
  Ubiquitous and Omnipresent

## Slide 24: Summary
    Understand Internet of Things
    Understand features and Infrastructure of IoT
In this lesson, you have learned: